## Slide 1: Integration of JVC/Kenwood's Exofield with auralization methods

## Slide 2: Contents
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Tests performed at ASK on a car with the road noise cancellation system
Alternative to Head Acoustics

## Slide 3: Contents
- Individualized HRTFs for Virtual Reality applications
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Current technology:
Background: a special test signal, the ESS - Exponential Sine Sweep
Background: the Kirkeby inversion method
- Binaural reproduction with stereo dipole (loudspeakers)
- Stereo reproduction with Exofield (headphones)
- Enhanced spatial reproduction inside vehicles
New technology:

## Slide 4: Measurement of a sound system
Nonlinear, time variant system
K[x(t)]
(loudspeakers)
Linear system
w(t)  h(t)
(propagation)
+
Noise n(t)
Input signal
x(t)
Distorted signal
w(t)
Output signal
y(t)
Desired result: linear impulse response of the acoustic propagation h(t)
x(t): known test signal played through loudspeakers (or headphones)
y(t): measured output signal
It is necessary to exclude the effect of the nonlinear part K and of the background noise n(t)
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 5: The test signal x(t): ESS
Input signal
x(t)
is a sine signal, which frequency is varied exponentially with time, starting at f1 and ending at f2 : EXPONENTIAL SINE SWEEP
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 6
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The test signal x(t): ESS

## Slide 7
Nonlinear, time variant system
K[x(t)]
(loudspeakers)
The nonlinear behaviour of the loudspeaker causes many harmonics to appear
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The system’s response y(t)

## Slide 8
Inverse filter z(t)
INVERSE SWEEP
Test Signal x(t)
Inverse Filter z(t)
The “time reversal mirror” technique: the inverse filter is the time-reversal of the test signal. As the log sine sweep has a spectrum falling down of 3 dB/Octave, proper equalization is required.
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The inverse filter z(t)

## Slide 9
Inverse filter z(t)
INVERSE SWEEP
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The inverse filter z(t)

## Slide 10
y(t)  z(t)
(deconvolution)
The measured signal y(t) is convolved with the inverse filter z(t). This operation causes a counter-clockwise rotation of time-frequency plane
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
y(t)*z(t)

## Slide 11
1°
2°
3°
5°
The previous are the harmonics distortion products of various orders
The last impulse response is the linear one
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
y(t)*z(t)
y(t)  z(t)
(deconvolution)

## Slide 12
After the sequence of impulse responses has been obtained, it is possible to automatically trim just the linear one:
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The linear impulse response h(t)

## Slide 13
Energy is spread over time: safer for loudspeakers
The deconvolution packs all the energy in a very short impulse response: S/N ratio gets a boost up to 70 dB or more !
Nonlinear effects are avoided
Measurement is very fast: for most applications a 10s sweep is long enough
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Benefits of the ESS signal

## Slide 14: The Kirkeby inversion
This operation is performed with the Kirkeby method in frequency domain [h(t) becomes H(f)]
In many cases the IR h(t) must be inverted, finding an inverse filter f(t) so that h(t)*f(t)=d(t)
A frequency-dependent regularization parameter b(f) is used
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 15: An example of using the Kirkeby inversion
The IR inversion can be used for correcting the response of a loudspeaker
The IR is inverted to obtain a pre-equalization filter
The music signal is realtime convolved with this pre-eq filter
This prefiltered signal corrects the loudspeaker and flattens the spectrum
A high quality omnidirectional mic is used to record the IR
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 16: An example of using the Kirkeby inversion
Before correction
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
After equalization

## Slide 17
Binaural recording and headphones playback
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Stereo Dipole
Binaural recording and loudspeakers playback

## Slide 18
10° angle between two Studio Monitors
Binaural out-ear microphones
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Stereo Dipole

## Slide 19
1. ESS test signal is played through each loudspeaker
2. The response is recorded by each binaural microphone
Sine sweep
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Ipse-lateral transfer function
Cross-talk transfer function
The Stereo Dipole
3. Four impulse responses are measured)

## Slide 20
3. Four impulse responses are obtained
4. IRs are inverted to get 4 filters
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Stereo Dipole
Kirkeby

## Slide 21
5. Filters and IRs are convolved to get a “Cross-talk cancelling effect”
Regularization parameter
At least 25dB of attenuation between direct and cross-talk contribution
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Stereo Dipole

## Slide 22
6. Preconvolving the signal with the Crosstalk cancelling filter, the sound played by a loudspeaker is listened only by the corresponding ear: cross-talk contribution are cancelled by each other
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Stereo Dipole

## Slide 23
h are measured in a standard stereo setup
to Headphones through eq filters
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Standard Exofield method

## Slide 24
Stereo configuration (60° angle)
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
The Standard Exofield method (UNIPR version)

## Slide 25
Measurement is very fast and robust to background noise
Non linearities of loudspeakers are avoided
Exofield with the ESS and Kirkeby:
Emulation of a stereo setup of two top-level studio monitors (Genelec) in a standard stereo setup
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Accurate equalization with inverse filters capable of correcting both magnitude and phase of the headphones
The Standard Exofield method (UNIPR version)

## Slide 26: Fundamentals of Ambisonics
The soundfield is decomposed in spherical harmonics of various order
Order_0
(omni mic)
Order_1
Order_2
Order_3
Three velocity components
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 27: Ambisonics microphone arrays
Microphone arrays are used for capturing spatial information
FOA – first order Ambisonics:
Soundfield
Ambeo
HOA – High order Ambisonics:
Eigenmike
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
RAI/AIDA
3DVMS

## Slide 28: First order Ambisonics (4 channels)
FOA microphones: allow for simultaneous measurements of the sound pressure (omni) and of the three Cartesian components of particle velocity (figure-of-8 patterns)
Pressure
Vx
Vy
Vz
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 29: High Order Ambisonics
HOA microphones: the Eigenmike allows for simultaneous recording of 32 signals, from which it is possible to derive spherical harmonics signals up to 4th order
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 30: Ambisonics encoding and decoding
Mic array
A-format
N x M
Encoding matrix
Encoding into spherical harmonics
B-format
M x K
Decoding matrix
Decoding to reproduction system
Loudspeakers
Headphones
Mic array: 4ch with FOA mics, 32ch with Eigenmike
B-format: 4ch for FOA, 16ch for 3rd order Ambisonics
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 31: Ambisonics encoding
N x M
Encoding matrix
A FIR filtering matrix, directly derived from anechoic measurements
n = 1…N
microphones
d = 1…D
directions
δ(t)
δ(t)
The A to B-format filter matrix is calculated inverting a set of IRs measured in anechoic room from 362 directions (SIR – Spatial Impulse Response), by means of Kirkeby.
Array placed on a 2-axis turning table
This processing technique is called 3DVMS and was developed by the RAI Research Center in Turin and AIDA, a spinoff of the University of Parma.
Depending on the purpose, a desired number M of VIRTUAL MICROPHONES can be obtained.
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 32: Ambisonics Decoding for loudspeakers
M x K
Decoding matrix
Also the decoding can be performed by means of a FIR filtering matrix
Loudspeakers system: an Ambisonics decoder is used with the desired number of output channels K (8 in this example) and optimized for the specific configuration (i.e.: Rapture3D from Blue Ripple Sound).
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 33: Ambisonics Decoding over headphones
M x K
Decoding matrix
The K speaker signals are convolved with the corresponding HRTFs
Headphones:
The past: generic HRTFs from dummy head (Neumann KU100)
Now: personal HRTFs thanks to EXOFIELD MICROPHONES
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
K x 2
HRTF matrix
*

## Slide 34: Ambisonics over headphones with Exofield
Now: EXOFIELD MICROPHONES
Immersivity
Naturalness
Spatial localization capability
All dramatically improved !
PERSONALIZED HRTFs
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 35: Realtime matrix convolution with X-volver
Our filtering engine is X-volver
X-volver is a VST plugin
Real time
Low CPU usage
Very high potential: capable of convolving the A-format (32 channels, 48 kHz, 32bit) with a 32x16 FIR filtering matrix (4096 samples each) to B-format (16 channels, 48 kHz, 32bit)
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 36: Ambisonics for VR
Why AMBISONICS ???
Virtual Reality
Augmented Reality
Mixed Reality
Videogames
Remote fruition of live events:
Concerts, sports…
360° panoramic tours
360° audio/video recordings reproduction
Enhanced listening experience
Low computational cost Head-tracking
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 37: Ambisonics for VR
Why AMBISONICS ???
Virtual Reality
Augmented Reality
Mixed Reality
Videogames
Remote fruition of live events:
Concerts, sports…
360° panoramic tours
360° audio/video recordings reproduction
Enhanced listening experience
Low computational cost Head-tracking
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 38: Panoramic video recording systems
Ricoh Theta V:
Easy-to-use
Cheap and compact
Automatic stitching
Includes the TA-1 FOA microphone array
Optional underwater case
8 GoPro ring:
Higher quality output
3D (stereoscopic) possible
Slow, offline stitching
No spatial audio recording
Incomplete vertical coverage
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 39: VR reproduction systems
High-level, top quality desktop solutions
Cheap, easy-to-use portable solutions
HTC VIVE
SAMSUNG ODISSEY
SAMSUNG GEAR VR
360 video with Ambisonics soundtrack
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
OCULUS GO

## Slide 40: From recording to HMD with head-tracking
X-volver FIR matrix
Ambisonics domain (1st or 3rd order )
Eigenmike™ 32
3-axis (counter) rotation
Ambisonics decoder (4x8 or 16x8 channels)
8x2 HRTF filter matrix for binaural rendering
HMD with standard headphones
Head tracking
Neumann KU100
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 41: Improvements with Exofield
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
16-speakers system. The standard cubic geometry has been enhanced adding an horizontal ring of 8 speakers
Individualised HRTFs personalised HRTFs instead of dummy head (Neumann KU100) HRTFs
Headphones equalization The headphones of the HMD are individually equalized over the head of each listener

## Slide 42: Improvements: the HRTF matrix can be asymmetrical
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Ambix-to-mid
Convolution matrix
B-format
Left/Right
Symmetrical harmonics
B-format
Left/Right
NOT Symmetrical harmonics
Ambix-to-side
Convolution matrix
+
Left ear
-
Right ear
Ambix-to-left
Convolution matrix
B-format
Ambix-to-right
Convolution matrix
Left ear
Right ear
MID-SIDE (Google)
symmetrical
TRUE STEREO (Exofield)
can be asymmetrical
B-format

## Slide 43: Improvements: headphones equalization
If Neumann KU100 HRTFs are employed, correction filters could be measured
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
with individualized HRTFs, the response of the HMD’s headphones must be measured on the subject wearing Exofield microphones
But no one is doing this, actually!
People listen to VR videos without taking care of equalizing the headphones being employed!

## Slide 44: Software for HTC Vive & Samsung Odyssey
Player based on Vive Cinema, an open source video player by HTC corporation
Equirectangular 360° video + 3rd order Ambisonics
Modified…
True-stereo convolution: Left and Right signals come from convolution with a full filter matrix, obtained convolving the Ambisonics decoding matrix and the HRTFs measured with Exofield microphones
HRTFs loading: measured HRTFs are read from .wav files (1st, 2nd, 3rd order, mono or stereo)
Mono convolution (mid-side stereo) with Neumann KU100 standard HRTFs
Fast switching: HRTFs sets can be switched on-the-fly during reproduction
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 45: Software for HTC Vive & Samsung Odyssey
PRO:
Highest quality of video reproduction (high resolution, refresh rate 90 Hz)
Very fast head-tracking sensors
CONS:
The HMD is expensive, not portable, cabling still required
High performances, very expensive computer needed
3rd order Ambisonics already implemented
Possibility to change HRTFs set on the fly
Double convolution: true stereo HRTFs supported
Low quality integrated headphones cannot be easily replaced with better ones
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 46: Software for Oculus GO – Samsung Gear VR
An Android app developed from scratch with UNITY and compiled with Oculus SDK
Equirectangular 360° video + 1st order Ambisonics
Resonance Audio engine for Ambisonics decoding (open source by Google)
Modified…
Standard plugin: binaural rendering is based on HRTFs measured with Neumann KU100
Our modified plugin: personalized HRTFs measured with EXOFIELD MICROPHONES are employed
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 47: Software for Oculus GO – Samsung Gear VR
PRO:
Portable solution of very good quality (refresh rate 60Hz)
Very affordable
CONS:
A specific app need to be recompiled for each set of HRTFs
File system not ready for 3rd order Ambisonics (Unity, max 8-channels)
Decoder ready for 3rd order Ambisonics (Resonance Audio engine)
Symmetric HRTF assumed (mid-side convolution)
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 48: Exofield Technology for automotive
BOSE headrest already on the market, but…
…WE CAN DO IT BETTER !
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 49: Exofield Technology for automotive
The concept: use Exofield microphones to bring inside vehicle a new advanced 3D audio system for cars
…WE CAN DO IT BETTER !
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 50: Exofield Technology for automotive
1. Target measurement in a listening room: a top quality 4.1 system
Two front stereo loudspeakers
Two rear surround loudspeakers
One subwoofer
Exofield microphones
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE

## Slide 51: Exofield Technology for automotive
2. Exofield measurement inside vehicle: the new ASK headrest + stereo dipole
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
ASK headrest 2.1
Exofield microphones
Stereo dipole

## Slide 52: Exofield Technology for automotive
Small distance from ears
Presence of head in between
No need to use cross-talk cancelling
ASK headrest: integrated subwoofer and two small surround loudspeakers
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Two side loudspeakers for surround
Integrated subwoofer for low frequencies (ASK patent pending)

## Slide 53: Exofield Technology for cars
Makes use of cross-talk cancellation previosly described
Frontal Stereo Dipole
Employed to recreate the front stereo system
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Already patented by ASK (Arletti, Nili, Farina, Ugolotti)
Front positioned (sun visor)

## Slide 54: Conclusions
INTRODUCTION BACKGROUND PAST vs PRESENT VIRTUAL REALITY THE FUTURE: INSIDE VEHICLE
Exofield microphones can be employed together with signal processing techniques developed at UNIPR (ESS, Kirkeby)
Exofield has been developed for standard stereo reproduction but Ambisonics technology is the current standard for spatial audio and VR/AR application (3D audio with head-tracking)
Thanks to Exofield, problems related to generic HRTFs have been solved, allowing for excellent playback of Ambisonics soundtracks over HMDs
Some experiments already demonstrated that also our past experience with Stereo Dipole can take great benefit from Exofield usage
Exofield could be the key for bringing to market a new 3D Audio system for vehicles: the already patented «Stereo Dipole inside cars» in combination with the new ASK headrest, individually tuned to each person by means of Exofield measurements

## Slide 55
END OF PRESENTATION
THANKS FOR ATTENTION